## Slide 1: Multimedia with VPU/IPU HW acceleration in Android
Oct 2012
Guoyin Chen

## Slide 2: VPU hardware spec
Decoding:
H.264 BP/CBP/MP/HP, VC-1 SP/MP/AP, MPEG-4 SP/ASP, H.263 P0/P3, MPEG 1/2 MP, Divx (Xvid) HP/PP/HTP/HDP, RV8/9/10, Sorenson Spark,VP8 (1280x720), AVS, H.264-MVC (1280x720), MJPEG BP (max. 8192x8192) up to full-HD 1920x1088 @30fps plus D1 @30fps
Encoding:
H.264 BP/CBP, MPEG-4 SP, H.263 P0/P3, MJPEG BP (max.8192x8192) encoding up to full-HD 1920x1088@30fps

## Slide 3: VPU in Andorid
VPU lib
VPU driver
VPU OMX
Dec/Enc Component
Stagefright Player/Recoder
GM Player/Recoder
Kernel
User Space
Android Default module
Freescale module

## Slide 4: VPU OMX Dec/Enc component in Andorid
Follow the OpenMAX IL 1.1.2 specification
Buffers allocated for Decoder component’s output port should be physical continuous
Buffers allocated for Encoder component’s input port should be physical continuous
Support below extension index in OMX API Get/SetParameter for stagefright integration
  "OMX.google.android.index.enableAndroidNativeBuffers“
  "OMX.google.android.index.getAndroidNativeBufferUsage“
  "OMX.google.android.index.storeMetaDataInBuffers“
  "OMX.google.android.index.useAndroidNativeBuffer"

## Slide 5: Video Render Acceleration(Single Display)
Max count of buffers in Video Surface may reach to 20 based on the codec profile
Max buffer size is about 3M(1920*1080*sizeof(NV12))
As how to allocate buffer for vpu omx component’s output port, reference the function OMXCodec::allocateOutputBuffersFromNativeWindow() in myandroid /frameworks/base / media/libstagefright/OMXCodec.cpp
VPU
GPU
IPU
Display Screen
Video Surface
FrameBuffer
UI Surface
MediaService
Surfaceflinger
Hardware Module
Physical Buffer
Software Module Instance
Android Service

## Slide 6: Video Render Acceleration
VPU
GPU
IPU
LVDS Screen
Video Surface
FrameBuffer0
UI Surface
MediaService
Surfaceflinger
Hardware Module
Physical Buffer
Software Module Instance
Android Service
IPU
FrameBuffer1
HDMI Screen

## Slide 7: Video Encoder acceleration
The buffer count in Camera Surface fixed to 6
Max buffer size is about 3M(1920*1080*sizeof(NV12)) based on the recorder config
The buffers in Camera Surface are shared among v4l2 capture driver, input buffer of VPU encoder component, and Camera Preview
VPU
IPU
Camera Sensor
Camera Surface
CameraService
MediaService
Hardware Module
Physical Buffer
Software Module Instance
Android Service

## Slide 8: IPU user case in Android
Update Framebuffer content to screen
Capture the image from camera sensor through CSI or MIPI